## Slide 1: CDA3101
Module 7: Cache Analysis Project

## Slide 2: Welcome!
Notes: ON SCREEN
Welcome back to CDA3101, Module 7. In this video we’ll talk about your cache analysis project.
[CLICK – Next Slide]

## Slide 3: Cache Analysis Project
For this assignment, you will design and implement a cache simulator. Your simulator will read a memory access trace from a file, determine whether each memory access is a hit or a miss, and output the hit rate.
You will then analyze the performance (hit rate) of three cache designs. You will do this in an analysis paper which should answer the following questions:
How does the performance of a cache change with its associativity? (e.g. direct mapped vs n-way associative vs fully associative)
How does the performance of a cache change with cache size?
How does the performance change with replacement policy?
Notes: OFF SCREEN
For this assignment, you will design and implement a cache simulator. Your simulator will read a memory access trace from a file, determine whether each memory access is a hit or a miss, and output the hit rate.
Your simulation can be written in whatever language you choose.
You will turn in a video screen capture showing your program compiling and running. [CLICK]
You will then analyze the performance (hit rate) of three cache designs. You will do this in an analysis paper which should answer the following questions: [CLICK]
  How does the performance of a cache change with its associativity? (e.g. direct mapped vs n-way associative vs fully associative) [CLICK]
  How does the performance of a cache change with cache size? [CLICK]
  How does the performance change with replacement policy?
[CLICK – Next Slide]

## Slide 4: Cache Analysis Project
Read a memory access trace from a file.
Trace files are located in
Files / Cache Analysis / Trace Files
Notes: OFF SCREEN
Your simulation needs to read a trace file.
Displayed on the right is a sample trace file.
There are trace files located in the directory shown.
You can use the smaller trace files for debugging, and the larger trace files for your simulation.
You are also welcome to create your own trace files.
[CLICK – Next Slide]

## Slide 5: Cache Analysis Project
Read a memory access trace from a file.
Trace files are located in
Files / Cache Analysis / Trace Files
Indicates whether the access is a load or store.
For this project, you can treat load and store the same. You can ignore this column.
Notes: OFF SCREEN
The first column in the trace file indicates whether the access is a load or store. [CLICK]
For this project, you can ignore this column. Load and store will be treated the same.
[CLICK – Next Slide]

## Slide 6: Cache Analysis Project
Read a memory access trace from a file.
Trace files are located in
Files / Cache Analysis / Trace Files
Indicates how many bytes are requested
For this project, you can ignore this column.
Notes: OFF SCREEN
The third column indicates how many bytes are requested. [CLICK]
For this project, we will not be concerned with how many bytes are requested. You can ignore this column.
[CLICK – Next Slide]

## Slide 7: Cache Analysis Project
Read a memory access trace from a file.
Trace files are located in
Files / Cache Analysis / Trace Files
This is the address.
This is what you care about.
Notes: OFF SCREEN
The middle column is the address. Your program needs to read the addresses.
[CLICK – Next Slide]

## Slide 8: Cache Analysis Project
OK, so I have an address. Now what do I do?
Each address will be split into:
Direct Mapped
Tag / Line / Offset
Set Associative
Tag / Set / Offset
Fully Associative
Tag / Offset
Each run through a trace file will need a cache design.
Notes: OFF SCREEN
After reading the address you will need to split it into appropriate fields.
Your cache design will determine the size of each of the fields.
You’ll need to translate the hex into a binary string, then split the string into fields. [CLICK]
Before reading the addresses, you’ll need to specify the cache design. Let’s talk about that next.
[CLICK – Next Slide]

## Slide 9: Cache Design Parameters
Cache Size
How many bytes in the cache?
Line / Block Size
How many bytes in a block / line?
Associativity
How many lines in a set?
These should be input parameters for a simulation run
Then, you should calculate the number of lines in the cache.
Notes: OFF SCREEN
There are three design parameters that will have to be specified for a simulation run: how many bytes are in the cache, how many bytes are in a block or line, and how many lines are in a set. Recall that one line per set is direct mapped, and all the lines in one set is fully associative. [CLICK]
From the specified parameters, you calculate the number of lines in the cache. This is the number of bytes in the cache divided by the number of bytes in a line.
[CLICK – Next Slide]

## Slide 10: Cache Design Parameters
Index | Set | Tag | Counter
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
… |  |  | 
Then you should create a data structure that simulates the cache.
Vector?
Array?
Map?
Notes: OFF SCREEN
Once you know the number of lines in the cache, you can create the data structure that models the cache. One idea is a vector which has an element for each line of the cache. Each element will have whatever information you need about that line, like the tag of the block currently in that line, the set number that that line is in, and a counter for when the block was placed there or accessed. This is a potential design, but the design is up to you.
[CLICK – Next Slide]

## Slide 11: Simulating the Cache
Index | Set | Tag | Counter
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
… |  |  | 
Once you have your data structure, read the addresses.
For each address:
Get tag and line or set (see example problems)
Map the address to where it could be in your data structure
Notes: OFF SCREEN
Once you have a data structure, you read each address in the trace file. For each address, get the tag and set number, go to the index in the data structure where the block should be.
[CLICK – Next Slide]

## Slide 12: Simulating the Cache: Direct Mapped
Example: Address = 0x1fffff78
Index | Set | Tag | Counter
0 | 0 |  | 
1 | 1 |  | 
2 | 2 |  | 
3 | 3 |  | 
4 | 4 |  | 
5 | 5 |  | 
6 | 6 |  | 
7 | 7 |  | 
Direct mapped, 512 byte cache, 64 byte line
lines in the cache
Offset = 6 bits, line = 3 bits, each line is a separate set.
Tag
0001 1111 1111 1111 1111 111
Line
101
Offset
11 1000
Hints / Suggestions
You can save the tag as a decimal number.
The offset is not used in this simulation.
Index | Set | Tag | Counter
0 | 0 |  | 
1 | 1 |  | 
2 | 2 |  | 
3 | 3 |  | 
4 | 4 |  | 
5 | 5 | 1048575 | 1
6 | 6 |  | 
7 | 7 |  | 
Notes: OFF SCREEN
Let’s look at an example.
The cache is direct mapped with 512 bytes in the cache, a 64 byte line size and 8 lines in the cache.
Our data structure is shown on the right. Since the cache is direct mapped, the set number is the same as the index. [CLICK]
The width of the offset field is log of 64, which is 8
The width of the line field is the log of the number of lines, or log of 8, which is 3
Translate the hex address to binary, then split into fields. [CLICK]
The line number is 7.
The tag is shown. [CLICK]
One suggestion is to translate the tag to decimal for easy storage and comparison. [CLICK]
Here is how the data structure looks after this access.
We’ll discuss the counter shortly.
[CLICK – Next Slide]

## Slide 13: Simulating the Cache: Fully Associative
Example: Address = 0x1fffff78
Index | Set | Tag | Counter
0 | 0 | 8388605 | 1
1 | 0 |  | 
2 | 0 |  | 
3 | 0 |  | 
4 | 0 |  | 
5 | 0 |  | 
6 | 0 |  | 
7 | 0 |  | 
Fully associative , 512 byte cache, 64 byte line
lines in the cache
Offset = 6 bits
Tag
0001 1111 1111 1111 1111 1111 01
Offset
11 1000
Hints / Suggestions
You can save the tag as a decimal number.
The offset is not used in this simulation.
Notes: OFF SCREEN
Here is an example with a fully associative cache.
Split the address into tag and offset
Since there is one set, start at the lowest index and search for an empty line.
Since the cache is empty, put it in the first line.
[CLICK – Next Slide]

## Slide 14: Simulating the Cache: Set Associative
Example: Address = 0x1fffff78
Index | Set | Tag | Counter
0 | 0 |  | 
1 | 0 |  | 
2 | 1 | 2097151 | 1
3 | 1 |  | 
4 | 2 |  | 
5 | 2 |  | 
6 | 3 |  | 
7 | 3 |  | 
Two way set associative, 512 byte cache, 64 byte line
lines in the cache
Offset = 6 bits
Tag
0001 1111 1111 1111 1111 1111
Set
01
Offset
11 1000
Hints / Suggestions
You can save the tag as a decimal number.
The offset is not used in this simulation.
Notes: OFF SCREEN
Here is a set associative example. The associativity is 2. The cache is 2-way set associative.
There are 8 lines and 4 sets. Set number is the floor of the line number divided by the associativity.
Since there are 4 lines, there are log of 4 equals 2 bits in the set field.
Split the address into tag, set, and offset.
The set number is 3. Look at the indices for set three, and if there is a vacant line, put the tag there.
[CLICK – Next Slide]

## Slide 15: Simulating the Cache
Index | Set | Tag | Counter
0 | 0 | 3323 | 7
1 | 0 | 444320 | 4
2 | 1 | 3420 | 2
3 | 1 |  | 
4 | 2 | 424242 | 1
5 | 2 |  | 
6 | 3 | 1048575 | 3
7 | 3 | 2300 | 10
Once you have your data structure, read the addresses.
For each address:
Get tag and line or set (see example problems)
Map the address to where it could be in your data structure
Look in the data structure to see if the block is already there (i.e. check tags)
If it is, it’s a hit.
If not, it’s a miss. Place block in cache.
Least recently used (LRU) vs. first in, first out (FIFO)
Notes: OFF SCREEN
Once the simulation has processed a number of addresses, your cache data structure will start to fill up. You need to process hits and misses.
When you map the address to where it should be in the data structure, you check the tag in every line where the block for that address could be. If there is a matching tag there is a hit.
If there is not a matching tag, it is a miss.
If any of the appropriate lines are empty, you can place the tag in that line.
If there are no empty lines, you will need to choose a line to have its entry replaced. If the cache is direct mapped there is only one choice, so you just replace that line.
If it is set associative or fully associative, you need to choose a block to replace. You should model two replacement strategies: least recently used, and first in, first out.
[CLICK – Next Slide]

## Slide 16: Counter Variable
Hit Rate
Increment a counter for each access
Increment a hit rate counter for each hit
Replacement Strategy
Save the access counter with the tag in the cache data structure
For least recently used, update the counter value in the cache line when there is a hit at the address with that tag
When choosing what to replace, choose the item with the oldest (smallest) counter
Notes: OFF SCREEN
To calculate the hit rate, and to determine which item has been in the cache the longest, implement a counter variable. Increment the counter with every address read.
Implement a separate hit counter. Increment the hit counter every time there is a hit.
The counter can also be used to determine which item to replace. Save the counter with the tag in the cache.
For the least recently used replacement strategy, update the value save with the tag every time there is a matching access request. When choosing which item to replace, choose the item with the smallest counter.
[CLICK – Next Slide]

## Slide 17: Ideas for Other Calculations
Index | Set | Tag | Counter
0 | 0 | 3323 | 7
1 | 0 | 444320 | 4
2 | 1 | 3420 | 2
3 | 1 |  | 
4 | 2 | 424242 | 1
5 | 2 |  | 
6 | 3 | 1048575 | 3
7 | 3 | 2300 | 10
Two way set associative 512 byte cache , 64 byte line,
8 lines in the cache
Address
0x1fff0023 (This is the 11th address processed.)
Tag
0001 1111 1111 1111 0000 0000
Set
00
Index | Set | Tag | Counter
0 | 0 | 3323 | 7
1 | 0 | 2096896 | 11
2 | 1 | 3420 | 2
3 | 1 |  | 
4 | 2 | 424242 | 1
5 | 2 |  | 
6 | 3 | 1048575 | 3
7 | 3 | 2300 | 10
Notes: OFF SCREEN
Here is our sample cache. Say that the address shown is requested, and this is the 11th, address processed, so the counter is 11.
The address maps to set 0. [CLICK]
Both lines in that set are full
Choose to replace index 1 because its counter is smaller. [CLICK]
Here is the updated cache.
[CLICK – Next Slide]

## Slide 18: Analysis
Vary a parameter and plot how the hit rate changes
Student result for 64 byte line size
Must discuss:
Effect of associativity
Effect of cache size
LRU vs. FIFO
Chart: Hit Rate vs. Cache Size for Different Cache Designs
| 1024 | 2048 | 4096 | 8192 | 16384
Direct Mapped | 0.83163 | 0.88957 | 0.94803 | 0.96374 | 0.98192
Fully Associative (FIFO) | 0.91427 | 0.95561 | 0.97838 | 0.98715 | 0.99058
Fully Associative (LRU) | 0.92606 | 0.96279 | 0.98354 | 0.98995 | 0.9919
2-Way Set Associative (FIFO) | 0.86285 | 0.89565 | 0.94896 | 0.97309 | 0.98065
2-Way Set Associative (LRU) | 0.88038 | 0.91142 | 0.9525 | 0.97404 | 0.9809
4-Way Set Associative (FIFO) | 0.88014 | 0.92605 | 0.95508 | 0.97607 | 0.98158
4-Way Set Associative (LRU) | 0.89328 | 0.93714 | 0.96089 | 0.97722 | 0.98196
8-Way Set Associative (FIFO) | 0.88062 | 0.93541 | 0.96397 | 0.97625 | 0.98174
8-Way Set Associative (LRU) | 0.89775 | 0.94351 | 0.96748 | 0.97771 | 0.98235
Notes: OFF SCREEN
Each run through a trace file is a data point. Vary a parameter, cache size or associativity, and plot how the hit rate changes.
Here is a sample student result for a 64 byte line size. They varied the cache size for a given associativity and replacement strategy and lines of hit rate versus cache size.
Create plots like this, or feel free to create plots of your choice. [CLICK]
You must discuss the effect of associativity, cache size, and replacement strategy.
Details on the report are found on the assignment page.
Good luck and have fun!
[CLICK – Next Slide]

## Slide 19: Wrap Up
Notes: ON SCREEN
Thanks for watching! That’s going to end this video.
[CLICK – Next Slide]

## Slide 20: Thank you for watching.